## Slide 1
Chaoyu Zhang
Department of Computer Science
Arkansas State University, USA
chaoyu.zhang@smail.astate.edu
Trusted Execution Environment: ARM TrustZone and IoT Security

## Slide 2: Outline
Introduction
    -Challenges and Motivation
Trust Execution Environment and TrustZone Overview
TrustZone System Architecture
-Secure Isolation Mechanism, Memory System,
-Monitor Mode, Secure Boot
TrustZone API
    -Client API,
    -Trusted Application and TEE API
Open-Source TEE and QEMU
SHARCS and TrustZone in SHARCS System IoT Layer
Conclusion

## Slide 3: Threaten in Traditional Rich OS Application Environment
Rich OS Environment
Applications
Kernel / Kernel Modules
Compromised Booting
Hardware Platform
System Libraries
Malware
﻿Attack surface is expanding
Malware could be hiding in the system
Vulnerability in booting process
might cause OS kernel compromise

## Slide 4: Threaten in Traditional Automotive Systems
Cars are becoming more vulnerable:
  Greater computer interaction with auto sensors
  Remote wireless connectivity and remote interaction
  Bridges to Controller Area Network (CAN)
Attackers have the privilege of selecting where to attack
Security researchers willing to spend years on high profile attacks

## Slide 5: Security Requirement for Automotive Systems

## Slide 6: Trusted Execution Environment
TEE guarantees code and data loaded inside to be protected with respect to confidentiality, integrity and availability.
TEE is an isolated execution environment provides isolated execution, integrity of applications with confidentiality of their assets.
TEE provides a higher level of security than a rich OS(operating system) and more functionality than an ASIC based secure element.

## Slide 7: Trusted Execution Environment
TrustZone

## Slide 8: Trusted Execution Environment

## Slide 9: ARM TrustZone Overview
Normal operations are in non-secure world execution, the secure world, and the non-secure world are converted through a Monitor mode
Normal world components cannot access secure world resources, secure world can access all the resource
Divide SoC hardware and software resources into Secure World and Normal World.
All operations that require confidentiality are performed in the secure world.

## Slide 10: ﻿ARM TrustZone Architecture
AMBA AXI bus propagates the NS bit outside the SoC
Peripherals and memory are configured during run time
TrustZone virtualizes each physical core into two cores

## Slide 11: TrustZone Architecture and Mechanism
AXI Bus
ARM Core
Interrupt Controller
TZASC
TZMA
TZPC
AXI-TO-APBB
Dynamic Memory Controller
DRAM
RAM
ROM
Peripherals
Memory isolation mechanism
Peripheral isolation mechanism

## Slide 12: ﻿TrustZone Processor Cluster Model
ARM Multiprocessor cluster has four physical cores, and each physical core has a secure virtual core and virtual non-secure core
The Non-secure virtual processor can only access Non-secure system resources, but the Secure virtual processor can see all resources
The NS bit's value on the main system bus is indirectly derived from the identity of the virtual core that performed the instruction or data access.

## Slide 13: ﻿TrustZone Memory System
MMU(Memory Manage Unit) maps the virtual address space to the physical address space outside of the processor.
Each world have their own virtual MMUs, manages the mapping of physical addresses.
One TLB (Translation lookaside buffer) shared by the two worlds.

## Slide 14: ﻿TrustZone Memory System
NS bit is to mark which world each item belongs to.
There is no need to refresh the TLB again when switching between the two worlds.
Caches has additional tag bit records the world and hold data from both sides.
There is no need to refresh the cache when switching between worlds

## Slide 15: ﻿TrustZone Monitor Mode
The monitor mode is a robust gatekeeper that manages the switches between the Secure and Non-secure processor states
No direct switching between the secure world and the non-secure world. All switching operations are performed through the Monitor Mode

## Slide 16: TrustZone Secure Boot
﻿Starts with trusted bootloader in ROM.
Cryptographic authenticate to each stage of the secure world boot process.
Assert the integrity of all the secure world software images that are executed. Prevent any unauthorized or maliciously modified software from running. s
﻿Public Key for the root of trust programmed into one time programmable on-chip memory.

## Slide 17: ﻿TrustZone API
Context
Rich OS (REE)
TEE Client API
Trusted OS
TEE Internal APIs
Client Application
Trusted Application
Session
Command
Shared Memory
Context: Connection from CA to the Trusted OS
Session: Connection from CA to the Trusted Application
Command: Unit of Communication from CA to TA
Shared Memory: Shared buffers allocated by Client API or by CA and registered

## Slide 18: ﻿TrustZone Client API
Principles:
Blocking functions
Can use from multiple concurrent threads in the CA
Can request cancellation
From another thread!
Client-side memory allocation
Pointers not opaque handles
Source-level portability but not binary
Implementation-specific data structures
Client API Functions (TEEC_xxx):
InitializeContext,
FinalizeContext
RegisterSharedMemory,
AllocateSharedMemory,
ReleaseSharedMemory
OpenSession, CloseSession
InvokeCommand,
RequestCancellation

## Slide 19: ﻿Trusted Application and TEE APIs
Trusted OS
TEE Internal APIs
Trusted Application
Entry Points:
Create
Destroy
OpenSession
CloseSession
InvokeCommand
TEE Core API:
●
Internal Client API
●
Property Access
●
Cancellation Support
●
Memory Management
●
Trusted Storage
●
Time
●
Cryptographic
●
Arithmetical
Other TEE APIs:
●
Trusted User Interface API
●
Secure Element API
●
Sockets API

## Slide 20: ﻿Trusted Application and TEE APIs
﻿Property Access GetPropertyAs[String, Bool, u32…] , Enumeration...
(Configuration Properties associated with TA, Client and TEE)
Cancellation Support GetCancellationFlag, MaskCancellation, UnMask...
Memory Management Malloc, Realloc, Free, MemMove...
Trusted Storage Create/Open/Close/…
TransientObject or PersistentObject
Time GetSystemTime/TAPersistentTime/REETime...
Cryptographic Cryptographic Functions: Message Digest, Symmetric Cipher, MAC, Authenticated Encryption, Asymmetric Encryption and Decryption, Key Derivation, Random Data Generation
Arithmetical Big Integer operations: Conversion, Logical, Basic Arithmetic, Modular Arithmetic...

## Slide 21: ﻿Trusted Application and TEE APIs
Trusted User Interface API TUICheckTextFormat,
TUIGetScreenInfo,
Create Message Box, PIN TUIInitSession/CloseSession Screen, Login Screen TUIDisplayScreen
Secure Element API Transport Level API:
SEServiceOpen, GetReaders…
Query the available Readers, SEReaderOpenSession...
Query the SEs in the SESessionOpenChannel…
Readers, SEChannelTransmit…
Exchange Data with the SEs
Service Level APIs: Discovery API, Secure Channel API
Sockets API open, close, send, recv,
error, ioctl

## Slide 22: OP-TEE: an Open-Source TEE
OP-TEE is an Implementation based on TrustZone technology.
Provides a shared basis for product TEE developments. Collaboration and consolidation not reinvention.
Provides a full example for research and education. Historically hard to learn about Trusted Environments
OP-TEE implements internal core API v1.1.x，which is an API exposed to trusted applications, and TEE Client API v1.0, an API that describes how to communicate with TEE.

## Slide 23: Getting Started with OP-TEE and QEMU
$ sudo apt-get install android-tools-fastboot autoconf bison cscope curl \
flex gdisk libc6:i386 libfdt-dev libglib2.0-dev \
libpixman-1-dev libstdc++6:i386 libz1:i386 netcat \
python-crypto python-serial uuid-dev xz-utils zlib1g-dev
$ sudo apt-get install ccache
$ mkdir -p $HOME/devel/optee
$ cd $HOME/devel/optee
$ repo init -u https://github.com/OP-TEE/manifest.git -m default.xml
$ repo sync
$ cd $HOME/devel/optee/build
$ make toolchains
$ make all run
Fetch the
Prerequisites
Fetch the Repos
Build and run!
Details: https://optee.readthedocs.io/en/latest/building/devices/qemu.html
QEMU is a free and open-source emulator and virtualizer.
We can use QEMU v7 to simulate Armv7-A processor for OP-TEE

## Slide 24: TrustZone Example
﻿Only allow authenticated users to interact
No passwords or secrets for the user
TrustZone based TEE can protect integrity/crypto on FIDO (Fast ID Online) “server” in car
TrustZone based TEE can protect private keys/crypto and FPS on phone

## Slide 25: IoT Challenges Traditional Cloud Storage
Fog Storage System
Cloud Storage Server
Applications on devices
IoT/Terminal Devices Disk
Applications on cloud
1. Stringent Latency Requirements
2. Network Bandwidth Constraints
3. Uninterrupted Services to Cloud
4. Massive Distributed IoT Devices Access Control
5. Protecting Resource-Constrained Devices (big data small power)
6. Massive Distributed Devices and On-board Systems Work securely
7. Devices Compromises Without Causing Intolerable Disruptions

## Slide 26: Motivation By Fog Architecture
Fog Layer
Parallel
ABE
IoT/ Terminal Devices Layer
Arm-TrustZone
Fog Storage
Cache
OpenSSL communication
OpenSSL communication
1 & 2. Low latency and high bandwidth network, data close to computation
3. Uninterrupted services by physical controllable network
4. Decentralized access control
5. Outsourcing ABE to HPC engine with parallelization
6. TEE and on-device cryptographic tools
7. TEE protection, multi-layer backup, devices disposable
Cloud Layer Storage Backup

## Slide 27: SHARCS (Secure Hierarchical Adaptive Reliable Cloud Storage) system Overview
Fog Layer
Cloud Storage layer
HPC
Engine
Fog Storage
System
Fog
Security
Controller
OpenSSL Layer
IoT/ Terminal Devices Layer
Arm-TrustZone
OpenSSL Layer
Untrusted Cloud
Services Provider
IoT Devices
Compromiser

## Slide 28: SHARCS HPC Engine

## Slide 29: SHARCS Fog Security Controller
Fog Security Controller
ABE
LBE
MPC
Advanced Security
Module
Symmetrical Encryption
Asymmetrical Encryption
Key Management
Cryptographic Module
Access Control
Homomorphic
Modular Design: change the scheme without modifying system architecture.
Scalable: for advanced security modules.
General Propose: supports basic cryptographic for security mechanism.

## Slide 30: SHARCS Fog Storage System
Cloud Layer: ciphertext backup for fault-tolerance and for sharing cross different fog servers.
Fog storage caching: for massive IoT devices uninterrupted connection and real-time access.
Disk-memory-cache fashion aims to reduce the network communication overhead with low latency and high-bandwidth.
Controllability: Fog Architecture gain more controllability to achieve better security and privacy protection.

## Slide 31: IoT Layer: ABE on TrustZone Implementation
Non-Secure Environment
Trusted Execution Environment
Non-Secure Applications
Non-Secure Rich OS
ARM Trusted Firmware
Hardware Platform
Hardware Secure Resource
TrustZone Client API
TrustZone Internal API
Trusted OS
ABE
Platin
Text
ABE
User
Policy
Related Crypto
graphic
Tools
OP-TEE

## Slide 32: Conclusion
TrustZone offers a dependable security platform. It provides scalability and an easily deployable solution for any device that supports the TrustZone architecture.
Using the TrustZone imposes low additional limitations on speed, memory, or computing power. The TrustZone relies on the device’s original processor and memory.
We simulated the IoT group equipped with TrustZone. It provides isolated execution, the integrity of applications, and confidentiality of the assets.
Though there are challenges in creating a scalable TEE eco-system. We believe the next generation of TEE-based solutions can leverage devices' protection from multiple threats and vulnerabilities.

## Slide 33
33
Thanks
Chaoyu Zhang
Department of Computer Science
Arkansas State University, USA
chaoyu.zhang@smail.astate.edu